CS4093 - Assignment 1
Alexander Stradnic - 119377263
XOR : An Exclusive OR gate works in a similar manner to OR, except that it only activates on one of the inputs only, not both.

A	B	Y
0	0	0
0	1	1
1	0	1
1	1	0

Verilog Code
module xor_gate (c,a,b); input a,b; output c; assign c = a^b; endmodule

Testbench Code
module xorgate; reg a; reg b; wire c; xor_gate TEST(.c(c), .a(a), .b(b)); initial begin $dumpfile("dump.vcd"); $dumpvars(1); a=0; b=0; #10; a=0; b=1; #10; a=1; b=0; #10; a=1; b=1; #10; end endmodule

Waveform

NAND : A NAND gate works by inverting the output taken from an AND gate.

A	B	Y
0	0	1
0	1	1
1	0	1
1	1	0

Verilog Code
module nand_gate (c,a,b); input a,b; output c; assign c = !(a&b); endmodule

Testbench Code:
module nandgate; reg a; reg b; wire c; nand_gate TEST(.c(c), .a(a), .b(b)); initial begin $dumpfile("dump.vcd"); $dumpvars(1); a=0; b=0; #10; a=0; b=1; #10; a=1; b=0; #10; a=1; b=1; #10; end endmodule

Waveform

NOR : A NOR gate works by inverting the output from an OR gate.

A	B	Y
0	0	1
0	1	0
1	0	0
1	1	0

Verilog Code
module nor_gate (c,a,b); input a,b; output c; assign c = !(a|b); endmodule

Testbench Code
module norgate; reg a; reg b; wire c; nor_gate TEST(.c(c), .a(a), .b(b)); initial begin $dumpfile("dump.vcd"); $dumpvars(1); a=0; b=0; #10; a=0; b=1; #10; a=1; b=0; #10; a=1; b=1; #10; end endmodule

Waveform

SR FLIP FLOP : An SR flip-flop can store a 1-bit value, and operates using 2 NAND gates. An input is designated as the setter (S) with the other input being the resetter (R).

S	R	Q	Q’	State
0	0	Q	Q’	No change
1	0	1	0	Set
0	1	0	1	Clear
1	1	X	X	Invalid

Verilog Code
module sr_flipflop(q,qbar,clk,s,r); input clk; input s; input r; output q,qbar; reg q,qbar; always @(posedge clk) begin if (r == 0 && s==0) begin q <= q; qbar <= qbar; end else if (s == 1 && r == 0) begin q <= 1; qbar <= 0; end else if (s == 1 && r == 1) begin q <= 1'bx; qbar <= 1'bx; end else if (s == 0 && r == 1) begin q <= 0; qbar <= 1; end end endmodule

Testbench Code
module TEST; reg clk,s,r; wire q,qbar; sr_flipflop TEST (.q(q), .qbar(qbar), .clk(clk), .s(s),.r(r)); initial begin $dumpfile("dump.vcd"); $dumpvars(1); clk=1; // initial r = 0; s = 0; #10; clk=0; // set but clock inactive r = 0; s = 1; #10; clk=1; // clock active, thus set works #10; clk=0; // reset but clock inactive r = 1; s = 0; #10; clk = 1; // reset activates #10; clk = 0; s = 1; // bad state but not active #10; clk = 1; // bad state activated #10; end endmodule

Waveform

JK FLIP FLOP : A JK flip-flop can store a 1-bit value, and operates using 2 NAND gates, in a similar manner to the SR flip-flop. The JK Flip-flop overcomes the issue with the SR flip-flop where the state is invalid when both inputs are set to 1 by flipping the state of the outputs in that instance.

J	K	Q	Q’	State
0	0	Q	Q’	No change
1	0	1	0	Set
0	1	0	1	Clear
1	1	~Q	~Q’	Toggle State

Verilog Code
module jk_flipflop(q,qbar,clk,j,k); input clk; input j; input k; output q,qbar; reg q,qbar; always @(posedge clk) begin if (j==0 && k==0) begin q <= ~q; qbar <= ~qbar; end else if (j == 1 && k == 0) begin q <= 1; qbar <= 0; end else if (j == 1 && k == 1) begin q <= ~q; qbar <= ~qbar; end else if (j == 0 && k == 1) begin q <= 0; qbar <= 1; end end endmodule

Testbench Code
module TEST; reg clk,j,k; wire q,qbar; jk_flipflop TEST (.q(q), .qbar(qbar), .clk(clk), .j(j),.k(k)); initial begin $dumpfile("dump.vcd"); $dumpvars(1); clk=1; // initial j = 0; k = 0; #10; clk=0; // set but clock inactive j = 0; k = 1; #10; clk=1; // clock active, thus set works #10; clk=0; // reset but clock inactive j = 1; k = 0; #10; clk = 1; // reset activates #10; clk = 0; k = 1; // bad state but not active #10; clk = 1; // bad state activated #10; end endmodule

Waveform

T FLIP FLOP : An T flip-flop can store a 1-bit value, and flips with the input (AND clock if relevant).

T	Q	Q’	State
0	Q	Q’	Hold State
1	~Q	~Q’	Toggle State

Verilog Code
module t_flipflop(q,qbar,clk,t); input clk; input t; output q,qbar; reg q,qbar; always @(posedge clk) begin if(q === 1'bx) begin q <= 1; qbar <= 0; end else if (t == 0) begin q <= q; qbar <= qbar; end else if (t == 1) begin q <= ~q; qbar <= ~qbar; end end endmodule

Testbench Code
module TEST; reg clk,t; wire q,qbar; t_flipflop TEST (.q(q), .qbar(qbar), .clk(clk), .t(t)); initial begin $dumpfile("dump.vcd"); $dumpvars(1); clk=1; // initial t = 0; #10; clk=0; // toggle but clock inactive t = 1; #10; clk=1; // clock active, thus toggle works #10; clk=0; // hold but clock inactive t = 0; #10; clk = 1; // hold 'activates' #10; clk = 0; t = 1; // toggle but not active #10; clk = 1; // toggle state activated #10; end endmodule

Waveform