CS4093 - Assignment 2
Alexander Stradnic - 119377263
Majority Gate: A Majority Gate takes in a set of inputs and returns the output of the majority of the input signals. For example, with 3 inputs, if 2 or more inputs are enabled, then the output is 1, vice versa when 2 or more are disabled.

A	B	C	Y
0	0	0	0
0	0	1	0
0	1	0	0
0	1	1	1
1	0	0	0
1	0	1	1
1	1	0	1
1	1	1	1

Verilog Code
module majority_gate (y,a,b,c); input a,b,c; output y; assign y = (a&&b)||(b&&c)||(a&&c); endmodule

Testbench Code
module TEST; reg a, b, c; wire y; majority_gate TEST (.y(y), .a(a), .b(b), .c(c)); initial begin $dumpfile("dump.vcd"); $dumpvars(1); a=0; b=0; c=0; #10; a=0; b=0; c=0; #10; a=0; b=1; c=0; #10; a=0; b=1; c=1; #10; a=1; b=0; c=0; #10; a=1; b=0; c=1; #10; a=1; b=1; c=0; #10; a=1; b=1; c=1; #10; end endmodule

Waveform

Full Adder: A Full Adder works in a similar manner to a half-adder, which takes two bits and outputs the sum and a carry if needed. However, an extra input is handled which is usually taken to be the carry bit from a previous adder.

A	B	Cin	Sum	Cout
0	0	0	0	0
0	0	1	1	0
0	1	0	1	0
0	1	1	0	1
1	0	0	1	0
1	0	1	0	1
1	1	0	0	1
1	1	1	1	1

Verilog Code
module full_adder (y,cout,a,b,c); input a,b,c; output y, cout; reg y, cout; always @(*) begin if(a + b + c == 0) begin y <= 0; cout <= 0; end else if(a + b + c == 1) begin y <= 1; cout <= 0; end else if(a + b + c == 2) begin y <= 0; cout <= 1; end else if(a + b + c == 3) begin y <= 1; cout <= 1; end end endmodule

Testbench Code:
module TEST; reg a, b, c; wire y, cout; full_adder TEST (.y(y), .cout(cout), .a(a), .b(b), .c(c)); initial begin $dumpfile("dump.vcd"); $dumpvars(1); a=0; b=0; c=0; #10; a=0; b=0; c=0; #10; a=0; b=1; c=0; #10; a=0; b=1; c=1; #10; a=1; b=0; c=0; #10; a=1; b=0; c=1; #10; a=1; b=1; c=0; #10; a=1; b=1; c=1; #10; end endmodule

Waveform

4:16 Encoder: A 4:16 Encoder works by converting an a series of 16 inputs to a 4-bit encoded number

I15	I14	I13	I12	I11	I10	I9	I8	I7	I6	I5	I4	I3	I2	I1	I0	O3	O2	O1	O0
0	0	0	0	0	0	0	0	0	0	0	0	0	0	0	1	0	0	0	0
0	0	0	0	0	0	0	0	0	0	0	0	0	0	1	0	0	0	0	1
0	0	0	0	0	0	0	0	0	0	0	0	0	1	0	0	0	0	1	0
0	0	0	0	0	0	0	0	0	0	0	0	1	0	0	0	0	0	1	1
0	0	0	0	0	0	0	0	0	0	0	1	0	0	0	0	0	1	0	0
0	0	0	0	0	0	0	0	0	0	1	0	0	0	0	0	0	1	0	1
0	0	0	0	0	0	0	0	0	1	0	0	0	0	0	0	0	1	1	0
0	0	0	0	0	0	0	0	1	0	0	0	0	0	0	0	0	1	1	1
0	0	0	0	0	0	0	1	0	0	0	0	0	0	0	0	1	0	0	0
0	0	0	0	0	0	1	0	0	0	0	0	0	0	0	0	1	0	0	1
0	0	0	0	0	1	0	0	0	0	0	0	0	0	0	0	1	0	1	0
0	0	0	0	1	0	0	0	0	0	0	0	0	0	0	0	1	0	1	1
0	0	0	1	0	0	0	0	0	0	0	0	0	0	0	0	1	1	0	0
0	0	1	0	0	0	0	0	0	0	0	0	0	0	0	0	1	1	0	1
0	1	0	0	0	0	0	0	0	0	0	0	0	0	0	0	1	1	1	0
1	0	0	0	0	0	0	0	0	0	0	0	0	0	0	0	1	1	1	1

Verilog Code
module encoder (i0,i1,i2,i3,i4,i5,i6,i7,i8,i9,i10,i11,i12,i13,i14,i15,o3,o2,o1,o0); input i0,i1,i2,i3,i4,i5,i6,i7,i8,i9,i10,i11,i12,i13,i14,i15; output o3,o2,o1,o0; reg o3,o2,o1,o0; always @(*) begin o0 <= 0; o1 <= 0; o2 <= 0; o3 <= 0; if(i1 | i3 | i5 | i7 | i9 | i11 | i13 | i15) begin o0 <= 1; end if(i2 | i3 | i6 | i7 | i10 | i11 | i14 | i15) begin o1 <= 1; end if(i4 | i5 | i6 | i7 | i12 | i13 | i14 | i15) begin o2 <= 1; end if(i8 | i9 | i10 | i11 | i12 | i13 | i14 | i15) begin o3 <= 1; end end endmodule

Testbench Code
module TEST; reg i0,i1,i2,i3,i4,i5,i6,i7,i8,i9,i10,i11,i12,i13,i14,i15; wire o3,o2,o1,o0; encoder TEST (.i0(i0), .i1(i1), .i2(i2), .i3(i3), .i4(i4), .i5(i5), .i6(i6), .i7(i7), .i8(i8), .i9(i9), .i10(i10), .i11(i11), .i12(i12), .i13(i13), .i14(i14), .i15(i15), .o3(o3), .o2(o2), .o1(o1), .o0(o0)); initial begin $dumpfile("dump.vcd"); $dumpvars(1); {i0, i1, i2, i3, i4, i5, i6, i7, i8, i9, i10, i11, i12, i13, i14, i15} = 16'b0; #10; i0 = 1; #10; i0 = 0; i1 = 1; #10; i1 = 0; i2 = 1; #10; i2 = 0; i3 = 1; #10; i3 = 0; i4 = 1; #10; i4 = 0; i5 = 1; #10; i5 = 0; i6 = 1; #10; i6 = 0; i7 = 1; #10; i7 = 0; i8 = 1; #10; i8 = 0; i9 = 1; #10; i9 = 0; i10 = 1; #10; i10 = 0; i11 = 1; #10; i11 = 0; i12 = 1; #10; i12 = 0; i13 = 1; #10; i13 = 0; i14 = 1; #10; i14 = 0; i15 = 1; #10; end endmodule

Waveform

Multiplexer: A multiplexer acts like a switch between inputs, using selector switch line(s) to choose which input is outputted.

A	B	C	D	S1	S0	Y
				0	0	A
				0	1	B
				1	0	C
				1	1	D

Verilog Code
module multiplexer (i0,i1,i2,i3,s0,s1,y); input i0,i1,i2,i3,s0,s1; output y; reg y; always @(*) begin if(s0) begin if(s1) begin y <= i3; end else begin y <= i1; end end else if(s1) begin y <= i2; end else begin y <= i0; end end endmodule

Testbench Code
module TEST; reg i0,i1,i2,i3,s0,s1; wire y; multiplexer TEST (.i0(i0), .i1(i1), .i2(i2), .i3(i3), .s0(s0), .s1(s1), .y(y)); initial begin $dumpfile("dump.vcd"); $dumpvars(1); i0 = 1; i1 = 1; {s0, s1, i2, i3} = 4'b0; // [s1][s0] = 00, inc from 00 to 11 #10; s0 = 1; #10; s0 = 0; s1 = 1; #10; s0 = 1; #10; end endmodule

Waveform

Demultiplexer: A demultiplexer acts in the opposite manner to a multiplexer, with a single input being routed to a selected output line.

Y	S1	S0	O0	O1	O2	O3
	0	0	Y	0	0	0
	0	1	0	Y	0	0
	1	0	0	0	Y	0
	1	1	0	0	0	Y

Verilog Code
module demultiplexer (o0,o1,o2,o3,s0,s1,y); input y,s0,s1; output o0,o1,o2,o3; reg o0,o1,o2,o3; always @(*) begin {o0, o1, o2, o3} = 4'b0; if(s0) begin if(s1) begin o3 <= y; end else begin o1 <= y; end end else if(s1) begin o2 <= y; end else begin o0 <= y; end end endmodule

Testbench Code
module TEST; reg y, s0, s1; wire o0, o1, o2, o3; demultiplexer TEST (.o0(o0), .o1(o1), .o2(o2), .o3(o3), .s0(s0), .s1(s1), .y(y)); initial begin $dumpfile("dump.vcd"); $dumpvars(1); y = 1; s0 = 0; s1 = 0; // [s1][s0] = 00, inc from 00 to 11 #10; s0 = 1; #10; s0 = 0; s1 = 1; #10; s0 = 1; #10; end endmodule

Waveform

Down Counter: A program which decrements an input (in this case, the hex number FFFF) to 0.

Verilog Code
module down_counter(input clk, reset, output[15:0] counter, output[15:0] counter2 ); reg [15:0] counter_down; reg[15:0] counter_down2; always @(posedge clk or posedge reset) begin if(reset) begin counter_down <= 8'hFF; counter_down2 <= 8'hFF; end else if (counter_down2 == 8'h00) begin counter_down <= counter_down - 8'h1; counter_down2 <= 8'hFF; end else begin counter_down2 <= counter_down2 - 8'h1; end end assign counter2 = counter_down2; assign counter = counter_down; endmodule

Testbench Code
module downcounter_testbench(); reg clk, reset; wire [15:0] counter; wire [15:0] counter2; down_counter dut(clk, reset, counter, counter2); integer iterations; initial begin $dumpfile("dump.vcd"); $dumpvars(1); clk=0; iterations = 0; while (iterations < (65536*2)) begin #5; iterations = iterations + 1; clk=~clk; end end initial begin reset=1; #20; reset=0; end endmodule